### License installation via the Univention Management Console: → UCS 3.x
- Log into the Univention Management Console with the Administrator account
- Click on the gear-wheel icon in the top right and then select Import new license.
- Select a license file with the Import license file button. Alternatively, you can enter a license key in the Import license as text field, e.g., using copy, and then convey it by clicking on the Import button.
- After a re-relogin the license is imported
### License installation for version 4.0-x and 4.1-x via the Univention Management Console- → UCS 4.0-x/4.1-x
- Log into the Univention Management Console with the Administrator account
- Click on the “Administrator” text in the top right and then select License and choose “import new license.”
- Select a license file with the Import license file button. Alternatively, you can enter a license key in the Import license as text field, e.g., using copy, and then convey it by clicking on the Import from text field button.
- After a re-relogin the license is imported
### License installation for version 4.2-x and 4.3-x via the Univention Management Console- → UCS 4.2-x/4.3-x
- Log into the Univention Management Console with the Administrator account
- Click on the three lines menu in the top right and then select License and choose “import new license.”
- Select a license file with the Import license file button. Alternatively, you can enter a license key in the Import license as text field, e.g., using copy, and then convey it by clicking on the Import from text field button.
- After a re-relogin the license is imported
### Installing a license via the command line (valid for all listed UCS Versions)
Log on to the master domain controller as the root user and then run the following command:
univention-license-import <license-file>
The following command can be used to display the license information in the command line:
univention-license-check